Sointula Waterworks District

Emergency Response Plan

2020

Sointula Waterworks Improvement District

Emergency Response Plan

Table of Contents

Page

Contact Numbers: Board and Staff	3

Emergency Contact Numbers	4

Type of Emergency

1. Broken water main	5

2. Power failure	5

3. Generator Failure	6

4. Complete pump failure at pump house	6

5. Contamination of water	7

6. Fire	8

7. Loss of source	8

8. Earthquake loss or structural damage	9

9. Flood conditions	9

Contact Information  Sointula Waterworks District

Chair:      Heather Orr: 	250-973-6506

Trustees:

Vern Aro: 	250-973-6798

Ross Weaver: 	250-973-6419

Virginia Goodwin:	250-973-6060

Ken Egan	250-230-3507

Office Manager:     Beverley Knox: 	778-206-0020

Maintenance Contractor:      John Brunet:   250-230-8468 (SWD cell)

250-973-6594 (home)

250-974-7005  (personal cell)

Back-up

Matt Preston   250-974-3523 home

John Huson:   250-902-3022 cell

VIHA  Eric Bergsma  (250) 902-6078  (Office)

(250) 230-0582 (cell)

Emergency Contact Numbers:

Maintenance and Repairs:

John Brunet: 250-973-6594

cell   250-230-8468

Personal cell  250-974-7005

Back up

Matt Preston   250-974-3523 home

John Huson:  250-902-3022

Electrician:

Andy Barlak: 250-973-6910

Backhoe operators:

Art Swanson: 250-973-6439,

cell: 250-974-8213

Delwin Nelson: 250-973-6725

Plumbers:

Mark Cunningham:  cell: 250-902-8199

Davin Holmes  250-202-6308

Guy Carlson: 250-973-6301

Clearance Krahn 1-403-586-5888

Bulk water haulers:

Delwin Nelson: 250-973-6725

Sewer technician (RDMW)

Alden Barnett: 250-974-7074

Malcolm Island Emergency Preparedness Team:

Linda Sowden, Team Leader: 250-973-6319

Tom Trimmer, Fire Chief: 250-973-6367

Medical Health Officer:

Dr. Charmaine Enns: Office: 250-331-8591

Public Health Engineer:

Murray Sexton: Office: 250-755-6215,

Fax: 250-755-3372

Environmental Health Officer:

Eric Bergsma: 250-902-6078, cell 250-230-0582, Fax 250-902-6072

VIHA, Port Hardy: Office: 250-949-3100, Fax: 250-949-2388

Emergencies: 1-800-204-6166

Ministry of Community, Sport, and Cultural Development:

Local Government Department:

1-250-356-6575

Advisory Services Branch:

1-250-387-4020

Police, Ambulance, and Fire: 911

BC Hydro: 1-888-769-3766

Port Hardy Radio Station: 1240CoastAM:

Phone: 250-949-6500, Fax 250 949 6580

Regional District of Mount Waddington: 250-956-3301, 250-956-3161

Sointula Resource Centre: 250-973-2001

Red Williams: 1-888-665-7802

250-248-5552  (cell)

Type of Emergency

1. Broken Water Main:

- Contact maintenance person

- Locate valve(s) and turn off

- Notify all users of interruption of service

- Arrange for repairs, disinfection and flush

- Take water samples

- Follow procedure outlined in s5. Contamination of water, where appropriate

- Take reading of reservoir water levels if necessary

- Advise local Public Health Office

- Arrange for alternate water source if necessary

- Notify Regional district staff, if necessary

Contacts:

- Sointula Waterworks Maintenance Contractors

- Sointula Waterworks Trustees, if necessary

- RDMW contact, if necessary

- Local Public Health Office

2. Power Failure:

- Contact maintenance person

- Call BC Hydro to determine time for power restoration

- Arrange for generator to be brought online as soon as possible

- Check reservoir levels at regular intervals

Contacts:

- Sointula Waterworks Maintenance Contractors

- BC Hydro

- Sointula Waterworks Trustees, if necessary

3. Generator failure

- Notify all users of interruption of water supply

- Notify all users to conserve water

- Advise Public Health Office

- Notify RDMW (Alden Barnett) regarding sewer if necessary

- Arrange for alternative water source, if required

- Contact local media for public service announcement if necessary.

Contacts:

- SWW maintenance contractor

- SWW trustees, if necessary

- Local Public Health Office

- RDMW contact, if necessary

4. Complete pump failure at pump house

- Contact maintenance to switch to alternate well

- Secure system at pump house

- Contact electrician

- Contact pump repair company

- Install spare pump if available

- Advise Local Public Health Office if interruption not short term

Contacts:

- SWW maintenance contractor

- SWW trustees, if necessary

- Electrician if necessary

- Red Williams

Local Public Health Office

5. Contamination of Water

- Notify SWW maintenance contractor

- Turn off pumps

- Notify affected users not to use water for domestic purposes,

- boil advisory, using signs at the ferry dock, small craft harbour, start of Kaleva Road and Bere Road;

- call water district residents using phone tree, post notices at the Co-op, Resource Centre, Post Office, and all public water access points

- Resource Centre to email their membership list

- Notify public health office

- If contamination occurs near the end of the water system, isolate from rest of system

- If entire system is contaminated, drain and shut down system

- Arrange for alternative water source if necessary

- Bring contractor out to clear water system lines

- Contact government agencies for advice and assistance

- Contact local media for public service announcement if necessary

Contacts:

- SWW maintenance contractor

- SWW trustees

- Malcolm Island Emergency Preparedness Team

- Ministry of Environment

- Local Public Health Office

- Provincial Emergency Preparedness, if necessary

- Others as necessary, depending on severity

6. Fire (Forest fire in water distribution area or fire fighting with system water):

- Notify SWW maintenance contractor

- Take reservoir water level reading

- Contact government agencies for advice and assistance, if necessary

- Notify all users of possible interruption of service

- Arrange for alternative water source if necessary

Contacts:

- Sointula Waterworks Maintenance Contractors

- Sointula Waterworks Trustees, if necessary

- Malcolm Island Emergency Preparedness Team, if necessary

- RDMW contact, if necessary

- Local Public Health Office

- Ministry of Environment

- Provincial Emergency Preparedness, if necessary

Others as necessary, depending on severity

7. Loss of source (water supply)

- Contact SWW maintenance contractor

- Ensure pumps are turned off

- Notify all users of loss of service

- Arrange for alternative water source if necessary

- Advise public health office

Contacts:

- Sointula Waterworks Maintenance Contractors

- Sointula Waterworks Trustees, if necessary

- Malcolm Island Emergency Preparedness Team, if necessary

- RDMW contact, if necessary

- Local Public Health Office

Ministry of Environment

8. Earthquake Loss or structural damage to system

- Contact SWW maintenance contractor

- Shut off the water lines. Close main in flow and out flow line from tank

- Arrange for volunteers to man the pumps

- Manually operate water system from pump houses

- Cycle pumps as required to maintain adequate pressure

- Advise public health office

- Notify all users of possible interruption of service

- Contact local media for public service announcement if necessary

- Arrange for alternate water source if necessary

- Arrange for structural engineer to assess damage

- Contact government agencies for advice and assistance

Contacts:

- SWW maintenance contractor

- SWW trustees, if necessary

- Malcolm Island Emergency Preparedness Team, if necessary

- Ministry of Environment

- Local Public Health Office

- Provincial Emergency Preparedness

- Others as necessary, depending on severity

9. Flood Conditions

- Contact SWW maintenance contractor

- Notify all users regarding the potential for water contamination, loss of pump, power etc.

- Users should be advised to store drinking water in advance, if possible, and to boil any suspect water for 2 minutes or disinfect with chlorine when flood conditions exist

- Arrange for alternative water source if necessary

- Contact local media for public service announcement if necessary

- Advise public health office

Contacts:

- SWW maintenance contractor

- SWW trustees, if necessary

- Malcolm Island Emergency Preparedness Team, if necessary

- Ministry of Environment

- Local Public Health Office

- Provincial Emergency Preparedness

- Others as necessary, depending on severity.

# Text boxes

The Old Medical Clinic

270-1st Street

Box 1

Sointula, BC, V0N 3E0

Phone: 250-973-2308

Email: sointula_water@yahoo.ca